## Slide 1
450 Rally Maintenance manuals
First Edition (February 2023)
This maintenance manual is copyrighted by TIBET NEW SUMMIT MOTORCYCLE CO.,LTD.
The contents and pictures of this maintenance manual are for reference only, please refer to the actual.
English
version
1

## Slide 2
Introduction
This motorcycle manual provides the reader with a detailed introduction to the basic structure, operating principles, disassembly and overhaul, and troubleshooting methods of the 450 Rally motorcycle. It also introduces the technical specifications, performance parameters and maintenance adjustment data of this model. It is hoped that this manual will provide technical support and guidance to the users and after-sales service personnel of Kaiyue motorcycles.
The technical specifications, performance parameters and maintenance adjustment data indicated in this manual are based on the latest status. Please note that any subsequent improvements made by the Company to this model may not be in accordance with this manual without prior notice. We sincerely hope that you will give us your valuable opinions and suggestions on the design, manufacture and quality of this model, and inform us for timely improvement.
All the information, charts and various data and performance indexes published in this manual are available until the printing of this manual. Please understand that TIBET NEW SUMMIT MOORCYCLE CO.,LTD., reserves the right to make changes to this manual without prior notice. Any part of this manual is the copyright of TIBET NEW SUMMIT MOTORCYCLE CO.,LTD. Otherwise, they will be held criminally and legally responsible.
Due to the limited level of the editor, there are inevitably errors and omissions in this manual, so please criticize and correct
TIBET NEW SUMMIT MOORCYCLE CO.,LTD.
Address: No. 2, Xiangyu Road, Shuangfengqiao Street, Yubei District, Chongqing
Customer service hotline :023-67842884
For more information, please visit our website at www.colovemotor.com
2
English
version

## Slide 3
Contents
Introduction
Chapter 1 Overview ....................................................................................................... 1
Chapter 2 Basic information ....................................................................................... 3
Chapter 3 Regular maintenance and adjustment .............................................. 28
Chapter 4 Frame, body trim, exhaust system ...................................................... 72
Chapter 5 EFI ................................................................................................................... 89
Chapter 6 Fuel System .............................................................................................. 124
Chapter 7 Cooling System ........................................................................................ 139
Chapter 8 Engine ......................................................................................................... 150
Chapter 9 Cylinder head assy ................................................................................ 158
Chapter 10 Cylinder block and piston ................................................................. 169
Chapter 11 Clutch, driving gear, overrunning clutch, oil pump, gearshift mechanism ..................................................................................................................... 175
Chapter 12 Magneto and balance driving and driven gear ......................... 187
Chapter 13 Crankcase, crankshaft, variable speed drive, balance shaft ... 193
Chapter 14 Front wheels, suspension, steering ................................................. 199
Chapter 15 Rear wheel, suspension........................................................................ 216
Chapter 16 Hydraulic brake system ....................................................................... 223
Chapter 17 ABS ............................................................................................................. 234
Chapter 18 Electrical parts ........................................................................................ 249
Chapter 19 Circuit schematic diagram ( factory ediion)..................................272
Chapter 20 Circuit schematic diagram (regular edition)..................................273
3
English
version

## Slide 4
How to use this manual
This manual describes the maintenance procedures for the 450 Rally.
Chapter 2 and 3 apply to the entire motorcycle. Chapter 4 describes the procedures for removing/installing components that may be used to perform the services described in the following sections. Chapter 3--Chapter 19 describe the motorcycle's components, grouped by location. If you are not familiar with this motorcycle, please read the technical characteristics in Chapter 2. Follow the recommendations of the maintenance schedule (Chapter 3) to ensure that the motorcycle is in optimum operating condition and that emission levels meet domestic environmental requirements, then go to the table of contents on the first page of that section. Most sections begin with program sets or system descriptions, maintenance information and troubleshooting. Detailed procedures are given on the next few pages. Refer to each section for troubleshooting based on the fault or symptom.
Your safety and the safety of others is very important. To help you make informed decisions, we have provided safety information and other information in this manual .
You must use your own good judgment. You will find important safety information in various forms, including.
Chapter 1
1
*Safety labels
*Safety Message - Precede the safety warning symbol with one of three signal words, i.e., DANGER, WARNING, or CAUTION. The meaning of these signal words is:
If you do not follow the instructions, death or serious injury will result.
Failure to follow instructions may result in death or serious injury.
If you do not follow instructions, you may be injured.
Instructions - How to properly and safely service this vehicle
English
version

## Slide 5
Symbol
The symbols used in this manual represent specific repair procedures. If additional information related to these symbols is required, it will be explained in detail in the text without using these symbols
 | Replace parts with new parts before assembly
 | Use recommended oils unless otherwise explanation
 | Use molybdenum oil solution (oil and molybdenum grease mixed in a ratio of 1:1)
 | Use multi-purpose high temperature extreme pressure compound lithium base grease (Youlicheng Grease SU-T330G/F or equivalent grease)
 | Molybdenum disulfide grease
 | Use molybdenum disulfide paste (40% or more molybdenum disulfide, NLGI #2 or equivalent). For example: G-n paste made by Dow Corning USA Honda Moly 60 (USA only). Rocol paste from Sumico Lubricants, Japan, manufactured by Rocol Ltd.
 | Use of silicone grease
 | Apply sealant. Use a medium strength sealant unless otherwise specified
 | Application of sealants
 | Use DOT4 brake fluid. Use recommended brake fluid unless otherwise stated
 | Use shock absorbing fluid
2
English
version

## Slide 6
Basic information
1 Maintenance rules ................................................................................................. 4
2 Model identification .............................................................................................. 5
3 Basic information ................................................................................................... 6
4 Torque value - engine part ............................................................................... 13
5 Torque value - body part .................................................................................. 15
6 Lubrication and sealing point - Engine part................................................ 26
7 Lubrication and sealing point - body part................................................... 27
3
English
version

## Slide 7
Maintenance rules
Please use genuine or KOVE recommended parts and lubricants or their equivalents for the KUVE. Parts that do not meet KOVE's design specifications may damage the motorcycle.
Use special tools designed for this product to avoid damage and incorrect assembly.
Use only metric tools when servicing the motorcycle. Metric bolts, nuts and bolts are not interchangeable with imperial fasteners.
Use new gaskets, O-rings, cotter pins and locking plates when reassembling.
When tightening bolts or nuts, start with large diameter or inner bolts. Then tighten in diagonal increments to the specified torque, unless a specific sequence is specified.
Clean parts with cleaner when disassembling. Lubricate all sliding surfaces before reassembly.
After reassembly, check all parts for proper installation and operation.
Route all wires as shown in the cable and cableway wiring.
Do not bend or twist control cables. Damaged control cables will not work properly and may become stuck or tangled.
Abbreviations
Throughout this manual, the following abbreviations are used to identify the respective components or systems.
Abbreviation | Full Name
ABS | Anti-lock braking system (450Rally factory version without ABS)
CKP sensor | crankshaft position sensor
DLC | Data link connector
DTC | Direct Torque Control
ECU | Engine control unit
ECT sensor | Engine coolant temperature sensor
EEP ROM | Electrically Erasable Programmable Read - Only Memory
EOP switch | Engine oil pressure switch
EVAP | Evaporative Emission Control System
IAT sensor | intake air temperature sensor
MAP sensor | ManifoldAbsolutePressureSensor
MCS | Motorcycle communication system
MIL | Malfunction Indicator Lamp
O2sensor | oxygen sensor
SCS Service connector | Service connector
TP sensor | throttle position sensor
VS sensor | vehicle speed sensor
4
English
version

## Slide 8
Model identification
factory edition-⑴ regular edition-⑵
⑴
⑵
5
English
version

## Slide 9
Basic information
items |  |  | specification
Size | Total lenght |  | 2190 mm
 | Total Width |  | 830 mm
 | Total height |  | 1487 mm
 | Axle distance |  | 1475 mm
 | Load free seat height |  | 960 mm
 | No load pedal height |  | 360 mm
 | No load ground clearance |  | 300 mm
 | Dry weight |  | 155 kg
 | Permissible maximum front axle load |  | 150 kg
 | Permissible maximum load on rear axle |  | 210 kg
 | Permissible maximum weight |  | 150 kg
Frame | Frame type |  | Cradle type frame
 | Front Suspension |  | Inverted telescopic fork
 | Front shock absorber stroke |  | 305 mm
 | Rear Suspension |  | External spring hydraulic
 | Rear shock absorber stroke |  | 117 mm
 | Front tire size |  | 90/90-21M/C
 | Rear tyre size |  | 140/80-18M/C
 | Front tyre brand |  | Zhengxin
 | Rear tyre brand |  | Zhengxin
 | Front Brake |  | Hydraulic single disc 298mm
 | Rear Brake |  | Hydraulic single disc 240mm
 | Caster angle |  | 28°
 | Towing distance |  | 122 mm
 | Fuel tank capacity |  | 31L
Engine | Cylinder alignment |  | 1 cylinder inline, 18° vertical tilt
 | Cylinder diameter and stroke |  | 94.5x64mm
 | Displacement |  | 499cm3
 | Compression ratio |  | 12.5:1
 | Air distribution system |  | Double overhead camshaft four-valve chain drive
 | intake valve | -5°BTDC | -5°BTDC
 |  | 35°ABDC | 35°ABDC
 | exhaust valve | 33°BBDC | 33°BBDC
 |  | -13°ATDC | -13°ATDC
 | lubricating system |  | Forced pressure lubrication + splash lubrication
 | Oil pump type |  | Oscillating type
 | Cooling system |  | water cooling
 | Air filltration |  | Paper cartridge，oil-based sponge
 | Engine dry weight |  | 37kg
 | Ignition sequence |  | /
 | Number of cylinder |  | single cylinder
6
English
version

## Slide 10
items |  |  | specification
The Fuel Supply System | Type |  | Bosch EFI
 | Throttle valve hole |  | 46mm
Drive system | Clutch system |  | Wet multichip type
 | Clutch operating system |  | Cable operation
 | Gearbox |  | Normal mesh two-stage transmission, 6-speed
 | Primary drive |  | 2.286（69/34）
 | Final drive |  | 3.769
 | Gear Ratio | 1th | 2.357（43/15）
 |  | 2th | 1.824 (46/14)
 |  | 3th | 1.474 (40/19)
 |  | 4th | 1.181(32/20)
 |  | 5th | 1.000(26/20)
 |  | 6th | 0.846(23/20)
 | Gear Shift Mode |  | international 1-N-2-3-4-5-6
Electricity | Ignition system |  | electron ignition
 | Starting system |  | electric starter
 | Charging system |  | Three-phase output magnetic motor
 | Regulator/rectifier |  | Three-phase full-wave rectification
 | Lighting System |  | Battery
items | specification
Engine idle | 1600±100rpm
ECT Sensor resistance（40°C/104°F） | 1.0-1.2kΩ
IAT Sensor resistance（20°C/68°F） | 2-4kΩ
Fuel injector resistance（20°C/68°F） | 11-13Ω
Oxygen sensor heater resistance（20°C/68°F） | 10-40Ω
Idle motor resistance（25°C/77°F） | 110-150Ω
items | specification
Sparking plug | CR8E（NGK）
Spark Plug Clearance | 0.80-0.90
Spark plug resistance | 5-8 KΩ
items | Standard value | limit value
Start motor brush length | 12.0-13.0（0.47-0.51） | 6.5（0.26）
EFI specification Measurement units：mm
Ignition system specification Measurement units：mm
Electric starter specifications Measurement units：mm
7
English
version

## Slide 11
Start motor brush length
cooling system
items |  | specification
Cooling capacity | radiator tank | 1.2 L
The radiator cap releases pressure |  | 108-133 kPa
Thermostat | Start turning on the temperature | 82±2℃
 | Fully open temperature | 92°C
 | valve lift | Not less than 8 mm
Recommended Antifreeze |  | Alcohol-free silicate coolant (Dongfeng Castrol LEC-II-25)）
Standard coolant concentration |  | 1:1 mixture with distilled water
Lubrication system specification
items |  | Standard value | limit value
engine oil capacity | After oil change | 1.4 L | -
 | After changing the oil filter | 1.6 L | -
 | After removing the engine | 1.8 L | 
Recommended engine oil |  | Recommended SG10W-50API service classification:SG or higher (except for oils marked as energy efficient on the round API service label)JASO T903 standard:MA viscosity:SAE 10W-50 | -
items |  | specification
hrottle body identification number |  | 450R
Fuel pressure at idle |  | 380Kpa±10kpa
Fuel pump flow (12V, 380kpa) |  | ≥30L/h
Fuel oil supply system | Type | Bosch EFI/
 | Throttle valve hole | 46mm
8
English
version

## Slide 12
9
items |  |  | Standard value | limit value
valve | Outside diameter of valve stem | Intake | φ5.472-φ5.487 | φ5.46
 |  | Exhaust | φ5.46-φ5.475 | φ5.44
 | Valve tube diameter | Intake | φ5.505-φ5.515 | φ5.535
 |  | Exhaust | φ5.505-φ5.515 | φ5.535
 | Valve stem and tube clearance | Intake | 0.018-0.043 | 0.07
 |  | Exhaust | 0.03-0.055 | 0.08
 | Valve seal tape width |  | 1.2 | ----
Cylinder Head | Planeness |  | 0.05 | 0.06
 | Width of valve seat working surface |  | 0.8 | ----
items | Standard value | limit value
Valve spring free length | outer:47.5 inner:38.1 | outer:47.35 inner:37.95
valve clearance | Intake:0.1-0.15 Exhaust:0.15-0.2 | Intake＞0.17 Exhaust＞0.22
Camshaft base circle run-out | 0.02 | 0.04
items |  |  | Standard value | limit value
cylinder | cylinder bore |  | φ94.5-φ94.52 | φ94.528
 | Out of roundness |  | 0.05 | 0.01
 | Flatness of cylinder surface |  | 0.03 | 0.05
Piston Piston ring Piston pin | piston outside diameter |  | φ94.453-φ94.467 | φ94.43
 | Inner diameter of piston pin hole |  | φ20.004-φ20.01 | φ20.015
 | Piston pin and piston pin bore clearance |  | 0.004-0 .018 | 0.025
 | Piston ring closing clearance | top ring/second ring | 0.2-0.35 | 0.5
 |  | oilring | 0.2-0.7 | 1.4
 | Piston ring and piston ring groove clearance | top ring | 0.03-0.07 | 0.08
 |  | second ring | 0.02-0.06 | 0.08
 | Clearance between cylinder and piston |  | 0.033-0.067 | 0.07
 | Outside diameter of piston pin |  | φ19.992-φ20 | φ19.99
Small end of connecting rod | inner diameter |  | φ20.015-φ20.025 | φ20.04
 | Clearance between small end of connecting rod and piston pin |  | 0.015-0.033 | 0.05
Cylinder body and piston specifications Measurement units：mm
Engine cylinder head/valve specification Measurement units：mm
English
version

## Slide 13
10
Shift fork/shift fork shaft/crankshaft/balance shaft specifications Measurement units：mm
items |  |  | Standard value | limit value
Shift fork | Internal diameter of the right fork of the secondary shaft / Internal diameter of the left fork of the secondary shaft |  | φ12.016-φ12.043 | φ12.045
 | Spindle fork inner diameter |  | φ12.016-φ12.043 | φ12.045
 | Jaw thickness |  | 4.8-4.9 | 4.8
shift fork shaft | Spindle fork shaft outer diameter |  | φ11.973-φ12 | φ11.95
 | Outside diameter of countershaft fork shaft |  | φ11.973-φ12 | φ11.95
 | cylindricity |  | 0.006 | ----
crankshaft | Connecting rod small end inner diameter |  | φ20.015-φ20.025 | φ20.04
 | Big end clearance of connecting rod | axial direction | 0.15-0.4 | 0.7
 |  | radial direction | 0.008-0.016 | 0.02
balance shaft | Shaft diameter |  | φ19.98-φ19.993 | φ19.96
Clutch/oil pump specifications Measurement units：mm
items |  | Standard value | limit value
Clutch handle free clearance |  | 10-20（0.4-0.8） | -
Clutch | Free spring length | 25 | 25
 | Friction plate free thickness | 2.95 - 3.05 | 2.85
 | Clutch driven plate flatness | 0.1 | 0.14
 | Clutch cover and friction plate clearance | 0.1 - 0.3 | 0.6
oil pump | Radial clearance between outer and inner rotors | 0.06 - 0.15 | 
 | End clearance between rotor assembly and cover plate | 0.04 - 0.1 | 
English
version

## Slide 14
Front wheel/suspension/steering specifications
items |  | Standard value | limit value
Tire Pressure | Vacuum tire（regular edition） | 200kPa(2.0kgf/cm³，29 psi) | -
 | Inner Tire（regular edition） | 100kPa(1.0kgf/cm³，15 psi) | -
Shaft Runout |  | ≤ 0.8 | 1.0
Rim Runout | radial direction | ≤ 0.8 | 1.0
 | end face | ≤ 0.8 | 1.0
Wheel dynamic balance |  | - | Max 60g
Front shock absorber | Free spring length/regular edition/factory edition | 475 mm | -
 | Recommended shock absorber oil | Special shock absorbing oil KHL 5W | -
 | shock absorberoil refill amount | 260ml in the damper, 300ml in the damping cylinder, total 560ml | -
Rear wheel/suspension specifications
items |  | Standard value | limit value
Tire Pressure | Vacuum tire（regular edition） | 200kPa(2.0kgf/cm³，29 psi) | -
 | Inner Tire（regular edition） | 100kPa(1.0kgf/cm³，15 psi) | -
Shaft Runout |  | ≤ 0.8 | 1.0
Rim Runout | radial direction | ≤ 0.8 | 1.0
 | axial direction | ≤ 0.8 | 1.0
Wheel dynamic balance |  | - | Max 60g
Rear shock absorber | Free spring length/regular edition/factory edition | 215mm/225mm | 
 | Recommended shock absorber oil | Special shock absorbing oil KHL 5W | 
 | shock absorberoil refill amount | 380ml | 
 | Cylinder nitrogen volume | 1.2mpa | 
driving chain | Size/link | AFAM520C2/114 | 
 | Looseness | 30-55 mm | 
Battery/charging system specifications
items |  |  | specification
Battery | type |  | MTX4L-FPP
 | capacity |  | 12V/4AH
 | Electrical leakage value |  | It can be stored at 25℃ for more than 1 year
 | voltage（28℃、68℉） | fully charged | >13.2V
 |  | need to be charged | <12.8V
 | Charge Current | normal | 2A
 |  | quick | 10A
Magnetor | charging capability |  | 280 W/9,000 rpm
 | Charging coil resistance（20°C/68°F） |  | 0.1-1.0Ω
11
English
version

## Slide 15
items |  | Standard value | limit value
Front Brakes | Specify brake fluid | DOT 4 | -
 | Brake disc wear indicator | - | To groove
 | Brake disc thickness | 4.0-4.01 | 3.5
 | Brake disc warped | - | 0.15
 | Main piston outer diameter | 11.000-11.050 | 11.060
 | Caliper piston cylinder outside diameter | 27.000-27.050 | 27.06
 | Caliper piston cylinder outside diameter | 30.200-30.250 | 30.260
Rear Brakes | Specified brake fluid | DOT 4 | -
 | Brake disc wear indicator | - | To groove
 | Brake disc thickness | 4.0-4.01 | -3.5
 | Brake disc warped | - | 0.15
 | Main piston outer diameter | 9.000-9.050 | 9.060
 | Caliper piston outside diameter | 22.620-22.670 | 22.680
Hydraulic brake specification Measurement units：mm
灯/仪表/开关规格
items |  | specification
Light | Automatic headlight (high/low light) | LED
 | Front turn signal/position light | LED
 | Rear turn signal light | LED
 | Brake/taillight | LED
 | License plate lamp | LED
 | Meter Light | LCD
 | Turn Signal Light | LED
 | Neutral indicator light | LCD
 | Engine oil pressure indicator | LCD
 | Coolant temperature high indicator | LCD
 | Malfunction Indicator Lamp（MIL） | LCD
 | ABS indicator | LCD
Fuse | Spare fuse | 15A,10A
 | Oil pump fan | 15A
 | FI | 10A
 | IGN fuse | 15A
 | Headlights start fuse | 15A
 | ABS2 fuse | 10A
 | ABS1 fuse | 15A
 | The above are regular edition fuse specifications, the following are factory edition fuse specifications | 
 | Spare fuse | 10A，10A
 | FI | 10A
 | Starting and horn | 10A
 | HEAD | 10A
 | FAN | 10A
ECT Sensor resistance | 40°C (104°F) | 1.0-1.3KΩ
 | 100°C (212°F) | 0.1-0.2KΩ
12
English
version
Light/meter/switch specification

## Slide 16
Type of fastener | Torque N.m | Type of fastener | Torque N.m
5mm screw bolt and nut | 6 | 5mm bolt | 5
6mm screw bolt and nut | 12 | 6mm bolt | 8
8mm screw bolt and nut | 22 | 6mm flange bolt(8mm head，Small flange） | 10
10mm screw bolt and nut | 60 | 6mm flange bolt（8mm head，big flange） | 12
12mm screw bolt and nut | 80 | 6mm flange bolt（10mm头）and nut | 12
 |  | 8mm flange screw bolt and nut | 22
 |  | 10mm flange screw bolt and nut | 60
items | QTY | diameter of screw mm | Torque N.m | Note
spark plug | 1 | 10 | 14 | 
Large visual hole cover | 1 | 30 | 5 | 
Small visual hole cover | 1 | 14 | 10 | 
Engine oil bolt | 1 | 16 | 24 | aluminium backing
Oil filter cover bolt | 2 | 6 | 7-19 | Apply proper amount of oil to the sealing ring
Oil strainer assembly bolt | 2 | 20 | 11-13 | Apply proper amount of oil to the sealing ring
items | QTY | Diameter of screw mm | Torque N.m | Note
Drain bolt | 1 | 6 | 10 | Copper Gasket
Thermostat cover bolt | 2 | 6 | 10 | 
Pump chamber bolt | 3 | 6 | 10 | 
water temperature sensor | 1 | 7 | 5-8 | 
items | QTY | Diameter of screw mm | Torque N.m | Note
cylinder head stud | 4 | 10 | 55-60 | Oil on thread and end face
cylinder head stud | 4 | 6 | 11-13 | 
Camshaft support bolt | 8 | 6 | 11-13 | 
Cylinder head bolt | 6 | 6 | 10-12 | 
Tensioner bolt | 2 | 6 | 11-13 | 
Tensioner bolt plug | 1 | 8 | 7-9 | 
Exhaust camshaft pressure reducing valve bolt | 1 | 6 | 10 | 
Listed below are the specifications apply to the specified torque fasteners. Other should tighten to the above standard torque values.
The standard torque value
13
Torque value - engine part
Cylinder head and valve torque
Cooling system torque value
Engine torque value
English
version

## Slide 17
Magneto and starting clutch torque
Box and driveline torque
items | QTY | Diameter of screw mm | Torque N.m | Note
Magneto rotor fastening nut | 1 | 10 | 80-90 | 
Magneto stator bolts | 2 | 5 | 7-9 | 
Trigger bolt | 2 | 5 | 7-9 | 
Left crankcase cover bolt | 8 | 6 | 11-13 | 
items | QTY | Diameter of screw mm | Torque N.m | Note
Chain plate | 2 | 6 | 11-13 | 
Tensioning plate bolt | 1 | 6 | 10 | 
Crankshaft bolts on both sides of closing case | 12 | 6 | 11-13 | Oil, replace the new bolt, fastening method see the following text
Fastening bolt for cover plate of left oil pump | 3 | 5 | 7-9 | 
Clutch and shift mechanism torque
items | QTY | Diameter of screw mm | Torque N.m | Note
Clutch fastening nut | 1 | 18 | 80-90 | Thread fastening glue
Clutch spring bolt | 4 | 6 | 8-10 | 
Drive gear fastening nut | 1 | 10 | 115-125 | Thread fastening glue
Shift mechanism positioning plate assembly | 1 | 6 | 11-13 | 
Right crankcase cover bolt | 11 | 6 | 11-13 | 
Five star plate bolt | 1 | 6 | 11-13 | 
14
Torque value of crankshaft, piston, cylinder block and balance shaft
items | QTY | Diameter of screw mm | Torque N.m | Note
Balancing shaft driven tooth fastening nut | 1 |  | 80-90 | 
Balancing shaft drive tooth fastening nut | 1 |  | 115-125 | 
English
version

## Slide 18
Torque value - body part
Installation area | Specification | Torsion N.m | Note
Self-tapping nails for the connection of the front brake fluid pipe pressure plate and the front shock absorbing trim | ST4.8 | 1 | 
Self-tapping nails for connecting rear fender liner and rear fender rear section | ST4.8 | 1 | 
Self-tapping nails for the connection between OBD and electrical bracket | M4.2 | 1 | 
Screws for connecting the lower cover plate of the rear mudguard rear section to the tail trim | M5 | 3 | 
Screws connecting the rear mudguard lower cover to the rear section of the rear fender | M5 | 3 | 
Internal six-flower countersunk head screws for connecting the fuel tank connector mounting plate to the left and right rear fuel tank | M5 | 5 | 
Oil level sensor mounting plate and the left fuel tank connected to the internal six flower countersunk head screws | M5 | 5 | 
Phillips pan head screw connecting oil pump to fuel tank | M5 | 5 | 
Phillips pan head screws for instrument and cowl bracket connection | M5 | 4 | 
Phillips pan head screw connecting the position light to the rear trim | M5 | 4 | 
Phillips pan head screw for connecting tail light to rear fender rear section | M5 | 4 | 
Inner six-flower step screw connecting rear tailcap to rear fuel tank | M5 | 4 | 
Inner six-flower step screw connecting the front fender to the front trim of the fuel tank | M5 | 4 | 
Internal six-flower countersunk head screw connecting the front gear ring to the front wheel drum | M5 | 5 | Threading glue
Crossed pan head screws for the rear brake pipe clamp to the flat fork | M5 | 5 | 
Inner six hexagonal flange face bolts connecting the rear harness clamps to the rear fuel tank | M5 | 4 | 
Inner six flower countersunk head screws for rear gear ring to rear drum connection | M5 | 5 | Threading glue
Crossed large pan head screws for the fuel filter mounting bracket to the fuel tank | M5 | 4 | 
Hexagon socket head cap screws for connecting headlight bracket pressure plate to headlight bracket | M5 | 4 | 
Phillips pan head screw for connecting the roll sensor to the electrical mounting bracket | M5 | 5 | 
Crossed large pan head screws connecting ECU to rear fuel tank | M5 | 4 | 
Internal hexagonal countersunk head screw connecting the seat cushion locking seat to the rear fuel tank | M6 | 8 | 
Hexagonal pan head step screw for front shock trim to front shock absorber | M6 | 5 | 
Crossed half-round head screws for the chain guard and flat fork connection | M6 | 8 | 
Hexagon socket flower pan head screws for connecting rear brake master cylinder to frame | M6 | 8 | 
Inner hexagonal countersunk head screws for connecting the rear fuel tank protection plate to the rear fuel tank | M6 | 8 | 
Inner six hexagonal flange face bolts for connecting electrical bracket to fuel tank reinforcement bracket | M6 | 12 | 
Inner six flower hexagonal flange face bolts connecting the electrical bracket to the rear fuel tank | M6 | 8 | 
Inner hexagonal flower pan head step screws for connecting headlight trim parts to headlight mounting brackets | M6 | 8 | 
Hexagon socket pan head step screws for connecting the water reservoir to the frame | M6 | 8 | 
15
Note: The following standard parts are for regular edition models only
English
version

## Slide 19
16
Installation area | Specification | Torsion N.m | Note
Hexagon socket flower-shaped pan head screws for connecting side bracket flameout switch to side bracket | M6 | 8 | 
Hexagon socket head screws for connecting the left and right front fuel tanks to the tank mounting bracket | M8 | 22 | 
Hexagon socket head screws in front of the left and right front fuel tanks connected to the frame | M8 | 22 | 
Hexagon socket head bolts connecting ignition lock to upper coupling plate | M8 | 22 | 
Inner hexagonal flange bolts connecting the left and right cowl brackets | M5 | 5 | 
Inner hexagonal flange bolts connecting the oil cooler grille to the lower shield | M5 | 5 | 
Inner hexagonal flange bolts connecting radiator grill to radiator | M5 | 5 | 
Inner hexagonal flange bolts connecting the shield mounting bracket to the left and right front fuel tanks | M5 | 5 | 
Inner hexagonal flange face bolts of the rear brake pedal connected to the rear brake rocker arm | M5 | 3 | Threading glue
Inner hexagonal flange bolts of headlight and headlight mounting bracket | M5 | 5 | 
Inner six hexagonal flange face bolts connecting the side bracket hook bracket to the rear fuel tank | M5 | 5 | 
Inner hexagonal flange bolts of the front brake main pump connected to the steering handle | M6 | 10 | 
Inner hexagonal flange bolts of the oil cooler connected to the frame | M6 | 12 | 
Hexagonal flange face bolts connecting the small sprocket cover to the engine | M6 | 8 | 
Inner hexagonal flange face bolts of muffler mounting bracket connected to rear fuel tank | M6 | 10 | 
Hexagonal flange face bolts with inner six flowers for connecting the lower shield to the frame | M6 | 12 | 
Hexagonal flange face bolts with inner six flowers connecting the hood bracket to the headlight bracket | M6 | 12 | 
Inner six hexagonal flange face bolts connecting the regulator to the electrical bracket | M6 | 10 | 
Inner hexagonal flange bolts of the radiator connected to the frame | M6 | 12 | 
Inner six hexagonal flange face bolts connecting the front brake fluid pipe clamp to the lower coupling plate | M6 | 10 | 
Inner six hexagonal flange face bolts connecting the front disc to the front wheel hub | M6 | 12 | Threading glue
Inner hexagonal flange face bolts of front fender to lower coupling plate | M6 | 8 | 
Inner hexagonal flange bolt for front ABS sensor mounting | M6 | 10 | 
Inner hexagonal flange bolt for connecting injector cap to throttle | M6 | 8 | 
Inner hexagonal flange bolt for clutch handle mounting and connection | M6 | 10 | 
Inner hexagonal flange bolt for connecting horn to frame | M6 | 12 | 
Inner six hexagonal flange face bolts connecting the air filter to the frame | M6 | 12 | 
Inner six hexagonal flange face bolts connecting the lower rear fuel tank mounting bracket to the rear fuel tank | M6 | 10 | 
Inner six hexagonal flange face bolts connecting the rear fuel tank reinforcement bracket to the rear fuel tank | M6 | 10 | 
Inner hexagonal flange bolts connecting the rear brake caliper trim to the rear brake caliper | M6 | 10 | 
English
version

## Slide 20
17
Installation area | Specification | Torsion N.m | Note
Inner six flower hexagonal flange face bolts for the connection of the rear disc brake disc to the wheel drum | M6 | 12 | Threading glue
Inner hexagonal flower pan head step bolts for the connection of the rear water skin to the rear fuel tank | M6 | 10 | 
Hexagonal flange face bolts for rear ABS sensor bracket to rear caliper bracket connection | M6 | 12 | 
Inner six flower hexagonal flange face bolts for the rear ABS sensor connected to the bracket | M6 | 8 | 
Inner six flower hexagonal flange face bolts for chain guide connection to flat fork | M6 | 10 | 
Inner hexagonal flange face bolt of headlight bracket connected to headlight module | M6 | 12 | 
Inner six hexagonal flange face bolts connecting the shift lever to the engine | M6 | 12 | 
Inner hexagonal flange surface bolts of ABS and ABS bracket | M6 | 12 | 
Inner hexagonal flange bolts of the left and right hood brackets connected to the frame | M8 | 22 | Threading glue
Hexagonal bolts connecting left and right chain adjustment | M8 | 10 | 
Hexagonal bolts with inner hexagonal flange for connecting the middle part of the muffler to the frame | M8 | 22 | 
Hexagonal bolts with inner hexagonal flange for connecting the rear part of muffler to the frame | M8 | 22 | 
Hexagonal bolts with inner hexagonal flange for connecting the lower coupling plate to the shock absorber | M8 | 22 | 
Rear bag mounting bolts connecting rear end cover and rear fender to rear fuel tank | M8 | 22 | 
Inner hexagonal flange bolts connecting the upper suspension plate to the frame | M8 | 35 | 
Inner hexagonal flange bolts of the upper coupling plate to the shock absorber | M8 | 22 | 
Inner six hexagonal flange face bolts connecting the upper mount to the lower mount | M8 | 22 | 
Inner hexagonal flange face bolts of the front brake caliper connected to the front shock absorber | M8 | 32 | Threading glue
Inner hexagonal flange face bolts of the front shock absorber connected to the front axle | M8 | 22 | 
Brake arm bolts for the rear brake arm connected to the frame | M8 | 22 | Threading glue
Rear fuel tank mounting bolts connecting the rear fuel tank to the frame | M8 | 22 | Threading glue
Hexagonal flange face bolts connecting the rear section of the rear fender to the rear fuel tank | M8 | 22 | 
Inner hexagonal flange face bolts of the front engine suspension plate connected to the fuel tank mounting bracket | M8 | 15 | 
Hexagonal flange face bolts of the front engine suspension plate connected to the frame | M8 | 22 | 
Sprocket bolt connecting sprocket to U-shaped rocker | M8 | 22 | 
Hexagonal bolt connecting oil level sensor to mounting plate | M10 | 22 | 
Hexagonal bolts with inner hexagonal flanges connecting the lower mount to the upper coupling plate | M10 | 35 | Threading glue
Flat head bolts connecting the rear shock to the triangular rocker | M10 | 44 | 
Hexagonal bolts with inner hexagonal flange for connecting the rear shock absorber to the frame | M10 | 44 | 
Hexagonal flange face bolts connecting the lower engine suspension to the engine | M10 | 54 | 
English
version

## Slide 21
18
Installation area | Specification | Torsion N.m | Note
Hexagonal flange face bolts of the engine upper suspension connected to the bracket | M10 | 60 | 
Hexagonal flange face bolts connecting the front engine suspension to the engine | M10 | 54 | 
Special bolts for side brackets connected to the frame | M10 | 2 | 
Hexagonal flange face bolts for connecting the U-shaped rocker to the frame | M10 | 60 | 
Flat head bolts for connecting triangle rocker to flat fork | M12 | 60 | 
Flat head bolts for connecting the U-shaped rocker to the triangular rocker | M12 | 60 | 
Hexagonal flange surface bolts connecting upper coupling plate to steering column | M14 | 80 | Lubricate with grease
Hexagonal flange face nut connecting the rear license plate light to the rear part of the rear fender | M5 | 5 | 
Hexagonal flange face self-locking nut for connecting the rear section of muffler to the bracket | M8 | 22 | 
Hexagonal flange face self-locking nut connecting the front engine suspension plate to the frame | M8 | 26 | 
Hexagonal flange face self-locking nut of the chain guide wheel and chain guide wheel bolt connection | M8 | 22 | 
Hexagonal flange face self-locking nut of the rear shock absorber connected to the triangle rocker | M10 | 60 | 
Hexagonal flange face self-locking nut of the lower engine suspension connected to the engine | M10 | 54 | 
Hexagonal flange face self-locking nut of the front engine suspension connected to the engine | M10 | 54 | 
Front wheel axle nut | M16 | 88 | 
Flat fork axle nut | M16 | 88 | 
Rear axle nut | M22 | 128 | 
4-slot adjusting nut for steering column locking connection | M25 | 40N-m, loose again 10N-m back 1/4 turn | 
English
version

## Slide 22
19
Installation area | Specification | Torsion N.m | Note
Front brake oil pipe pressure plate and front shock trim attachment screw | ST4.8X12 | 3N·m | 
Rear mudguard lower cover and tail trim attachment screw | ST4.8X15/16 | 2N·m | 
Front and rear oil cup filler cap fastening screws | M4 | 3N·m | 
OBD and electrical bracket connecting bolts | M4.2X13 | 1N·m | 
Front brake upper pump oil cup cover fastening screw | M4x12 | 3N·m | 
Small instrument and road book bracket connection nut | M5X0.8X5*8 | 4N·m | 
Instrument indicator and road book bracket attachment nut | M5X0.8X5*8 | 4N·m | 
Rear position light/tail light mounting screw | Crossed pan head screws M5X12 | 6N·m | 
Oil pump and fuel tank connecting bolt | M5X20 | 6N·m | 
Headlight adjustment controller and handlebar connection bolt | M5x10 | 10N·m | 
Battery positive and negative cable bolts | M5X10 | 4N·m | 
Oil pipe fitting mounting plate and left and right rear fuel tank connecting bolts | M5X10 | 6N·m | TC4 titanium alloy
Oil level sensor mounting plate and left fuel tank connection screw | M5X10 | 2N·m | TC4 titanium alloy
Hand windshield and hand windshield bracket | M5X10(Step diameter 8X height 3.5) | 5N·m | 
Brake pedal and brake arm connecting bolt | M5x12 | 5N·m | (Threading glue)TC4 titanium alloy
Oil-cooling grille and lower shield connecting bolt | M5x12 | 5N·m | TC4 titanium alloy
Rear brake card oil pipe clamping screw | M5X12 | 5N·m | TC4 titanium alloy
Fuel filter bracket and left fuel tank attachment screw | M5X12 | 4N·m | TC4 titanium alloy
Side bracket hook bracket and fuel tank mounting bolts | M5X12 | 5N·m | TC4 titanium alloy
Front fuel tank guard trim bracket left and right and fuel tank connecting bolts | M5X12 | 6N·m | TC4 titanium alloy
Road book and road book bracket connecting bolts | M5X16/25 | 4N·m | TC4 titanium alloy
Note: The following standard parts are for factory edition models only
English
version

## Slide 23
20
Installation area | Specification | Torsion N.m | Note
Air filter cotton and air filter housing fastening bolts | M5X78 | 4N·m | 
Throttle cable adjusting nut | M6 | 5N·m | 
Clutch handle adjusting nut | M6 | 2N·m | 
Starter relay nut and main line connecting bolt | M6 | 5N·m | 
Main wire tower wire and engine connection bolt | M6 | 10N·m | 
Chain retainer and flat fork attachment screw | M6*12，Head diameter10.5 | 8N·m | TC4 titanium alloy
Front windshield and windshield mounting bolts | M6,self-locking nut | 12N·m | 
Front reduction trim cover and front reduction attachment screw | M6X10,stepping 8.5X3.5 | 8N·m | TC4 titanium alloy
Front brake disc and wheel hub attachment bolt | M6x12 | 12N·m | Threading glueTC4 titanium alloy
Headlight module and cowl bracket attachment bolts | M6x12 | 12N·m | TC4 titanium alloy
Air filter and frame attachment bolts | M6X12 | 10N·m | TC4 titanium alloy
Horn and frame attachment bolts | M6X12 | 12N·m | TC4 titanium alloy
Lower guard and emergency water bottle connecting bolt | M6x12 | 12N·m | TC4 titanium alloy
Bolts connecting the front brake oil pipe clamp to the upper and lower coupling plate | M6X12 | 10N·m | TC4 titanium alloy
Rear fuel tank protective cover with rear fuel tank mounting screws | M6X12 | 6N·m | TC4 titanium alloy
Rear ABS sensor and bracket mounting screw Head cover bracket and road book bracket attachment bolt | M6X12 | 8N·m | TC4 titanium alloy
Head cover bracket and road book bracket attachment bolt | M6X12 nut M6X10.4 | 8N·m | 
Chain guide rear bolt and flat fork connecting bolt | M6X12，pan 11 | 10N·m | TC4 titanium alloy
Rear water barrier rubber with rear fuel tank connecting bolt | M6X12,stepping8.5X3.5 | 8N·m | TC4 titanium alloy
Headlight cover trim with headlight mounting bracket attachment bolt | M6X12,stepping8.5X3.5 | 8N·m | TC4 titanium alloy
Bolts connecting the secondary water bottle to the frame | M6X12,stepping8.5X3.5 | 8N·m | TC4 titanium alloy
Head cover bracket and road book bracket 1 connecting bolt | M6x13 | 10N·m | TC4 titanium alloy
Muffler mounting bracket and rear fuel tank connecting bolt | M6X13 | 10N·m | TC4 titanium alloy
Bolts connecting the lower shield to the frame | M6x13 | 12N·m | TC4 titanium alloy
English
version

## Slide 24
21
Installation area | Specification | Torsion N.m | Note
Headlight mounting bracket and cowl bracket attachment bolt | M6X13 | 10N·m | TC4 titanium alloy
Rear brake disc trim and flat fork attachment bolts | M6X13 | 10N·m | TC4 titanium alloy
Rear brake caliper trim and rear caliper attachment bolt | M6X13， | 10N·m | TC4 titanium alloy
Rear fuel tank mounting bracket and rear fuel tank attachment bolt | M6X13，pam14 | 10N·m | TC4 titanium alloy
Rear fuel tank lower mounting bracket and rear fuel tank attachment bolt | M6X13，pan14 | 10N·m | TC4 titanium alloy
Steering damper bracket and frame attachment bolt | M6x16 | 12N·m | TC4 titanium alloy
Rear brake master cylinder to frame attachment bolt | M6x16 | 12N·m | TC4 titanium alloy
Rear brake disc and rear wheel hub attachment bolts | M6X16 | 12N·m | TC4 titanium alloy
Hand windshield bracket and clutch handle bracket/brake handle bracket attachment bolts | M6X20 | 8N·m | 
Bolts connecting steering damper to upper connecting plate | M6x20 | 10N·m | TC4 titanium alloy
Front brake pump and brake handle mount attachment bolt | M6x20 | 10N·m | TC4 titanium alloy
Fuel filler and handle bolts | M6x20 | 10N·m | TC4 titanium alloy
Clutch handle mount bolt with handlebar | M6x20 | 10N·m | TC4 titanium alloy
Instrument operation switch and handgrip connecting bolt | M6x20 | 10N·m | TC4 titanium alloy
Shifter and engine connecting bolt | M6X20 | 12N·m | TC4 titanium alloy
Front mudguard and lower connecting plate connecting bolt | M6X20 | 10N·m | TC4 titanium alloy
Injector cap and throttle fastening bolt | M6X20 | 8N·m | TC4 titanium alloy
Seat cushion lock and rear fuel tank mounting bolts | M6X20 | 8N·m | TC4 titanium alloy
Electrical mounting bracket and frame attachment bolt | M6X20，pan11 | 12N·m | TC4 titanium alloy
Oil cooler and frame bolts | M6X25 | 12N·m | TC4 titanium alloy
Bolts connecting the left and right radiators to the frame | M6X25 | 12N·m | TC4 titanium alloy
Bolts connecting the regulator to the electrical bracket | M6X25 | 12N·m | TC4 titanium alloy
Left and right radiator lower bolts to frame | M6X25 | 12N·m | TC4 titanium alloy
Small sprocket cover and engine mounting bolts | M6X30 | 10N·m | TC4 titanium alloy
Chain guide box front bolt and flat fork attachment bolt | M6X48，pan 11 | 10N·m | TC4 titanium alloy
Head cover bracket and road book bracket fastening nut | GB/T 6187 self-locking nut，M6 | 8N·m | 
English
version

## Slide 25
22
Installation area | Specification | Torsion N.m | Note
Rear tank vent fitting screws | Screw thread with M6 | 4N·m | 
Headlamp bracket and head cover bracket connection bolt (rubber) | Rubber bolt M6X12 nut M6X10 | 8N·m | 
Frame and air filter housing connection bolt | Rubber bolt M6X12 nut M6X10 | 8N·m | 
The left and right sides of the front fuel tank are connected to the underframe nut | Rubber bolt M8X20 nut M8 | 22N·m | 
Guide sprocket self-locking nut and guide sprocket connecting bolt | self-locking nut，M8X1.25 | 22N·m | 
Connection bolts under front fuel tank to frame | Inside M8, outside M16*1*11, length 35.5mm | 22N·m | TC4 titanium alloy
Tail trim piece with tank 2 mounting bolts | Hex shaped Step Bolt M8X15 Step 5.5 | 22N·m | TC4 titanium alloy
Flat fork chain adjustment lock nut | M8 | 22N·m | 
Clutch cable lower adjustment nut | M8 | 8N·m | 
Muffler collar | M8 | 22N·m | 
Oil cooler overoiling bolt installation | M10/copper packing | 25N·m | 
Brake arm bolt to frame connection bolt | M8 x 16 Step 18.2 Hex Socket Step Bolts | 22N·m | Threading glue TC4 titanium alloy
A cap nut for connecting the front muffler segment to the engine | M8X1.25X14 | 22N·m | 
Front tank mounting bracket bolts left and right | M8X10 | 15N·m | TC4 titanium alloy
Rear tank mounting bolts | M8X11 stepping 25mm | 22N·m | TC4 titanium alloy
The front engine suspension is bolted to the frame | M8x115 | 26N·m | TC4 titanium alloy
Engine suspension with frame connection bolt | M8x16 | 36N·m | TC4 titanium alloy
Mounting point on front tank with frame connection bolt | M8X20 | 22N·m | TC4 titanium alloy
Front bottom reduction barrel locking bolt | M8x25 | 22N·m | TC4 titanium alloy
Bolts are connected to rear oil tank in rear block | M8X25 | 22N·m | TC4 titanium alloy
English
version

## Slide 26
23
Installation area | Specification | Torsion N.m | Note
Front tank side mounting point with frame connection bolt | M8X30 | 22N·m | TC4 titanium alloy
Upper connecting plate and damping fastening bolt | M8x35 | 22N·m | TC4 titanium alloy
Front brake caliper with bottom barrel bracket connection bolt | M8x35 | 32N·m | (Threading glue)TC4 titanium alloy
Muffler middle section and frame connection bolt | M8X35 | 22N·m | TC4 titanium alloy
Lower connecting plate with damping fastening bolt | M8x40 | 22N·m | TC4 titanium alloy
Muffler rear section and bracket connection bolt | M8X45 | 22N·m | TC4 titanium alloy
Hand windscreen bracket left and right handlebar connection bolts | M8X45 | 22N·m | TC4 titanium alloy
Fasten the upper and lower bracket bolts in the direction | M8x50 | 22N·m | TC4 titanium alloy
Head cover bracket and frame connection bolt | M8x50 | 22N·m | TC4 titanium alloy
Connecting bolt between guide sprocket and U-shaped shake frame | Inner hole M10, length 61, | 60N·m | TC4 titanium alloy
Triangle shake frame and rear reducer lower connection bolt | M10 x 45 flat head bolt Shaped bolt Ducro | 60N·m | 
Front engine suspension with engine connection bolts | M10x1.25x115 | 54N·m | TC4 titanium alloy
Lower engine rear suspension with frame connection bolts | M10x1.25x130 | 54N·m | TC4 titanium alloy
U-shaped shaking frame and frame connection bolt | M10x1.25x130 | 60N·m | 
Lower engine front suspension with frame connection bolts | M10x1.25x145 | 54N·m | TC4 titanium alloy
Brake tubing to front brake caliper connection bolt | M10x1.25x22 | 30N·m | TC4 titanium alloy
The brake tubing is bolted to the front brake upper pump | M10x1.25x22 | 22N·m | TC4 titanium alloy
Brake tubing and rear brake pump, caliper connection bolt | M10X1.25x22 | 22N·m | TC4 titanium alloy
English
version

## Slide 27
24
Installation area | Specification | Torsion N.m | Note
Brake tubing and rear brake upper pump connection bolt | M10X1.25x22 | 22N·m | TC4 titanium alloy
Engine sprocket fastening nut | M10X22 | 45N·m | 
Engine suspension with engine connection bolt | M10x30x1.25 | 54N·m | TC4 titanium alloy
Direction handle lower holder connection bolt | M10x35 | 34N·m | TC4 titanium alloy
Side bracket and frame connection special bolt | M10x42.3 | First 10N·m, then loosen 1/3 turn, clamping bolt and nut 60N·m | TC4 titanium alloy
Connecting bolt to frame above rear shock absorption | M10x52 | 44N·m | TC4 titanium alloy
U-shaped shaking frame and triangle shaking frame connection bolt | M12X105 Flat head bolt shaped bolt | 60N·m | TC4 titanium alloy
Connecting bolt between flat fork and triangular rocking frame | M12X85 Flat head bolt shaped bolt | 60N·m | TC4 titanium alloy
Upper coupling plate and direction column fastening bolt | M14x1.5x30 | 80N·m | （Thread oiling）
The front oil tank is fitted with hexagonal nuts and connected to the frame | M16X1，3mm thickness | 35N·m | TC4 titanium alloy
Front axle lock nut | M16x1.5 | 88N·m | TC4 titanium alloy
Flat fork shaft fastening nut | M16x1.5 | 88N·m | TC4 titanium alloy
Oxygen sensor and muffler front section connection bolt | M18 | 44N·m | 
Rear axle lock nut | M22X1.5 | 128N·m | 
The directional post locks the four-slot nut | M25x1 | 40N·m first, 10N·m loose, and then a quarter turn | 
English
version

## Slide 28
25
Installation area | Specification | Torsion N.m | Note
Headlamp bracket press plate mounting bolt | M5X12 | 4N·m | TC4 titanium alloy
Headlight and headlight bracket mounting bolts | M5X12 | 5N·m | TC4 titanium alloy
ECU to rear tank connection bolt | M5X12 | 4N·m | TC4 titanium alloy
Radiator grille with radiator connection bolt | M5X12 | 5N·m | TC4 titanium alloy
Rear tail cover with fuel tank 1 Mounting screws | M5X13,stepping 8X3.5 | 5N·m | TC4 titanium alloy
Connecting screw between side guard plate and windshield glass | M5X13,stepping 8X3.5 | 4N·m | TC4 titanium alloy
Roll sensor and electrical mounting bracket connection bolt | M5X16 | 4N·m | TC4 titanium alloy
English
version

## Slide 29
Lubrication and sealing point - Engine part
Materials |  | Location | Note
seal gum | 1596 | Crankcase coupling surface | 
 | 1590 | Magneto outlet | 
engine oil |  | The whole surface of the inner and outer rotors of the oil pump | 
 |  | Valve rod sliding face and rod end | 
 |  | Timing chain the entire surface | 
 |  | Camshaft rolling surface | 
 |  | Inner surface of cylinder bore | 
 |  | Piston outer surface, piston pin hole and piston ring groove | 
 |  | Outer surface of piston pin | 
 |  | The whole face of the piston ring | 
 |  | Clutch friction disc entire surface | 
 |  | Clutch pull rod sliding surface | 
 |  | Shift shaft rod part and dial plate | 
 |  | Double gear shaft whole face | 
 |  | Start clutch whole face | 
 |  | The entire surface of the fork shaft | 
 |  | Crankshaft connecting rod big end bearing inner surface | 
 |  | Crankshaft connecting rod small end hole | 
 |  | Gear teeth (primary drive, crankcase, starting reduction) | 
 |  | Disk tooth sliding surface | 
 |  | Each bearing rotation area | 
 |  | Surface of each O-ring seal | 
Molybdenum disulfide oil |  | tappet column | 
 |  | Camshaft surface | 
 |  | Cylinder head CAM shaft hole | 
Multi-purpose grease |  | Starter motor seal ring | 
 |  | Speed sensor seal ring | 
 |  | Large and small decorative cover seals | 
Degreasing agent |  | All joint surfaces | 
26
English
version

## Slide 30
Materials | Location | Note
Lithium base multi-purpose extreme pressure grease NLGI2# | Steering bearing ring sliding surface | 3-5 grams each（0.1-0.2oz）
 | Dust seal for steering bearing | 
Multi-purpose grease | Side support rotating shaft sliding area | 
 | Seat latch sliding area | 
 | Throttle door handle pull slot and roll up area | 
 | Clutch lever slide area | 
 | Front axle rod and wheel dust ring rotation area | 
 | Rear axle rod and dust ring rotation area | 
 | Rear wheel hub left O-ring | 
 | Rear shock absorber upper slip area | 
 | U-shaped frame rotation area and needle roller bearings | 
 | Tripod rotation area and needle roller bearings | 
 | Rear flat fork shaft rod and plane bearing, needle roller bearing | 
 | Guide sprocket mounting stud sliding face | 
 | Brake arm bolt rotation area | 
Silicone grease | Front brake caliper rubber sleeve sliding area | 
 | Front brake caliper bracket pin sliding area | 
 | Front brake caliper piston dust-proof oil seal contact area | 
 | Front brake handle mounting bolt contact area | 
 | Rear brake caliper bracket pin sliding area | 
 | Rear brake caliper rubber sleeve sliding area | 
 | Contact area between rear master cylinder push rod and main piston | 
 | Rear brake pump dust jacket pushrod mounting area | 
 | Rear brake caliper dust ring contact area | 
Brake fluid | Brake main piston and leather bowl | 
 | Front and rear main pump hose connector O-ring | 
 | Brake caliper piston oil seal | 
 | Brake clamp piston outer surface | 
 | Brake pipe joint nut thread | 
Cable lubricant | Clutch cable | 
 | Seat lock cable | 
Special damping fluid KHL 5 W | Front damping oil seal lip | 
 | Front damping and dust proof seal lip | 
 | Front shock absorbing end cover O ring | 
KOVE special chain lube or equivalent | Whole surface of chain | 
Sealant (Loctite 263 Made by Loctite) | Driving tooth fastening nut | 
 | Clutch fastening nut | 
 | Balanced driven tooth fastening nut | 
 | Balancing drive tooth fastening nut | 
 | Magneto rotor fastening nut | 
Low strength locking agent | Front and rear brake pad mounting bolts | 
 | Rear and rear ABS ring mounting bolts | 
 | Brake arm and brake pedal mounting screws | 
 | Front engine suspension left and right with Rubber bolt | 
Lubrication and sealing point - Body part
27
English
version